SECTION 11 6600

### PART 1 GENERAL

  - RELATED WORK

Review Contract Documents for requirements that affect work of this section. Specification sections that directly relate to work of this section include, but are not limited to:

Section 33 3000 – Site Improvements

Section 32 1826 - Synthetic Grass Surfacing

Section 32 1822 – Synthetic Athletic & Sports Surfacing

Section 12 9300 – Site Furnishings

Section 03 3000 – Cast-in-Place Concrete

Section 11 6500 – Athletic & Recreational Equipment

1.02	SUBMITTALS

A. Product Data: Submit manufacturer’s product literature, technical specifications, and other data required to demonstrate compliance with specified requirements for all athletic equipment.

1.03	QUALITY ASSURANCE

A. Fabrication and installation of site improvements by experienced craftsmen with excellent record of performance on completed projects of comparable size, scope, and quality.

B. All materials, hardware and furnishings shall be new, first quality.

1.04	FIELD MEASUREMENTS

A. Contractor shall verify position and layout of all athletic field equipment. Verify dimensions by field measurements.

  - SYSTEM DESCRIPTION

- Tennis nets, posts, and accessories.

### PART 2 PRODUCTS

2.01 TENNIS EQUIPMENT

A. Base; manufacturers and product selections named are provided to establish the minimum standard, and shall be as supplied by:

SportsEdge®

259 Murdock Rd.

Troutman, NC 28166

PH: 800-334-6057

info@sportsedge.com

www.sportsedge.com

B. COMPONENTS

1. TENNIS POSTS, Round: (Specifier select model) Round Tennis Post Model #SETPR.

A. 3” Round tubular steel w/ integral lacing bars.

B. Brass Winder

C. Polyester Powder Coated.

D. Galvanized steel ground sleeve.

E. Color: Green or Black. (Specifier select color)

2. TENNIS POSTS, Square: (Specifier select model) Square Post Model #SETPS.

A. 3” Square box steel w/ integral lacing bars.

B. Brass Winder

C. Polyester Powder Coated.

D. Galvanized steel ground sleeve.

E. Color: Green or Black. (Specifier select color)

3. TENNIS NET: Model #SETN30LS

A. 3.5mm braided polyethylene tapered net body.

B. Fiberglass dowels.

C. Plastic coated steel cable.

D. Heavy duty white vinyl coated 4 stitched headbands.

4. CENTER STRAP & ANCHOR: Model #SETSA

A. Polyester center strap.

B. Heavy duty galvanized steel ground anchor.

### PART 3 EXECUTION

3.01 INSTALLATION OF EQUIPMENT

A. All athletic equipment shall be installed as recommended with manufacturer's written directions, and as indicated on the drawings.

END OF SECTION