SECTION 02880

PART 1 – GENERAL

1.01	SUMMARY

A. This section may include, but is not limited to the following track & field equipment:

1. Shot Put Ring

2. Toe Board

3. Discus Ring

4. Discus Cage, Rear Entry

5. Shot Cage

6. Pole Vault Box / Cover

7. Long Jump Pits / Covers

8. Take-Off Boards

9. High Jump Pad

10. Pole Vault Pad

11. Lane Gates

B. Related Sections: Review Contract Documents for requirements that affect work of this section. Specification sections that directly relate to work of this section include, but are not limited to:

Section 02542 - Synthetic Grass & Turf

Section 02790 - Athletic & Recreational Surfaces

Section 02870 – Site Furnishings

Section 03300 – Cast in Place Concrete

Section 11480 - Athletic, Recreational and Therapeutic Equipment

1.02	SUBMITTALS

A. Product Data: Submit manufacturer’s product literature, technical specifications, and other data 	     required to demonstrate compliance with specified requirements for all athletic equipment.

1.03	QUALITY ASSURANCE

A. Fabrication and installation of site improvements by experienced craftsmen with excellent record of performance on completed projects of comparable size, scope, and quality.

B. All materials, hardware and furnishings shall be new, first quality.

1.04	FIELD MEASUREMENTS

A. Contractor shall verify position and layout of track and field equipment. Verify dimensions by field measurements.

PART 2 – PRODUCTS

2.01	MANUFACTURERS

A. Manufacturers and product selections named are provided to establish the minimum standard and shall comply with NFHS requirements.

Equipment shall be as supplied by:

SportsEdge®

P.O. Box 837,  259 Murdock Rd.

Troutman, NC 28166

PH: 800-334-6057

info@sportsedge.com

www.sportsedge.com

2.02	TRACK AND FIELD EQUIPMENT

A. General: Provide equipment complying with requirements in NFHS rule book.

A. Shot Put / Hammer Circle:

1. Model # SE374, Aluminum Shot / Hammer Circle consisting of 2" x 2" x 1/4", aluminum angle that is roll bent to a 42" [106.7cm] radius. Use with #SE363 cast aluminum shot toeboard for a depressed pad.

B. Toe Board:

1. Model # SE363, Aluminum, for depressed concrete pad.

C. Discus Ring:

1. Model # SE375, Discus Circle consists of 2" x 2" x 1/4", aluminum angle roll bent to a 49 7/32" [125.0cm] radius.

D. Discus Cage:

1. Model # SE8021, High School Discus Cage with Rear Entry System. Net shall have a special cut out and extra section in the back to allow for safer and easier access to the throwing circle. The rear entry discus cage shall have the following attributes:

a. Main upright poles: (7) to be 2 7/8” O.D. round .203” thick wall 6063-T6 aluminum tube, b. Cable: vinyl coated net support cable to reduce net sag

c. Main Net: weather treated nylon, #42 knotless, 180 lb test, hinged net arms, at ground level to hold the net in place at the front of the cage.

d. Barrier Net: include additional 8’ tall barrier net #SE80212 for added safety.

e. Ground sleeve, 30" deep

E. Shot Cage:

1. Model # SE805, High School, 4 main upright poles to be 2.5” Square 14ga. Steel powder coated White, 180 lb. test nylon weather treated netting, vinyl coated steel cable running throughout the top to reduce sag, net secured at ground level with (4) stakes, include 20” deep ground sleeves.

F. Pole Vault Box with Cover:

1. Vault Box: Model SE507 SKYDEX™ Soft Vaulter’s Box to provide increased safety. Vault box to have peak Gmax of (G: 99) from a fall height of 17’-6”.

a. Tray: 1/8” molded fiberglass with a white gel coated interior, back of the box is reinforced by steel molded into the fiberglass tray

b. Cover: made of thermoformed (white) high molecular weight polyethylene 1/8” sheet, designed to be filled with track surface so the area around the box will match the color of the track surface

2. Vault Box Lid: Model SE50701, steel

G. Long Jump Pit Forming System and Cover Set

1. Model #SE519-3211, with Aluminum Pit Cover Set.

a. Aluminum long / triple jump pit form, including base forms, cover ledges, accessories, 		 	    	and pit covers. Aluminum pit cover assembly with 0.5” (13mm) recessed top surface.

H.  Long Jump Take-Off Board System:

1. Adjustable Long Jump & Triple Jump Take-Off Board Systems:  Model No. SE444

a. Aluminum Tray:  Constructed of 3/16” thick aluminum, formed and welded.

b. Aluminum Base Board: Constructed of 1/8” aluminum sheet (3003), formed to shape. All adjustment screws are stainless steel. The base board can be adjusted for level and height, using six adjustment screws, without removing the base board from the tray. There are four threaded fasteners for attaching the take-off board.

c. Wood Take-Off Board: Constructed of ¾” A/B marine grade plywood with a white outdoor enamel coating. There are four counter-sunk holes for mounting to the base board. The take-off board is finished on both sides so that it can be reversible.

I. High Jump Pad:

1. Model # SE640A ESSENTIALS® with #SE640A02 Vinyl Weather Cover, meets high school specifications, to have the following attributes:

a. Skirted mesh top to hold the units together for a snug fit.

b. Royal Blue.

c. Specification Compliance: NFHS

d. Overall size: 16’ x 8’ x 24” (Overall size metric: 4.88m x 2.44m x .61m),

Base Units (2): 8’ x 8’ x 24”

J. Pole Vault Pit Pad:

1. Model # SE653 ESSENTIALS® with #SE65302 Vinyl Weather Cover, #SE717 Planting Box Safety Collar and having the following attributes:

a. Skirted mesh top to hold the units together for a snug fit.  Includes recommended preferred landing zone.

b. Royal Blue.

c. Specification Compliance: NFHS

d. Overall size: 19’9” x 20’2” x 26” (Overall size metric: 6.02m x 6.15m x .66m)

(3) Base Units: 6’7” x 12’9” x 26”

(2) Front Slant Units: 8’3” x 7’5” x 26”

K. Lane Gates:

1. Model # SE854, shall be aluminum, lift & rotate, locks in place, includes ground sleeves.

PART 3: EXECUTION

3.03 INSTALLATION

A.  All athletic equipment shall be installed as recommended by manufacturer's written directions, and as indicated on the drawings.

-- END OF SECTION --